## Slide 1: VNX Profile - MAA-VNX01
Project:
09/21/2020, 01:14 (UTC +02:00)
Everon Maria, everon.maria@dell.com
Pascal Bemelmans, pascal.bemelmans@l1.nl
1139403
MAA-VNX01
Project ID:
Prepared For:
Prepared By:
Created:
PPTX 2018.08.14
Copyright © 2020 Dell Inc.

## Slide 2: Common Summary: Inventory, Capacity and Workload
Serial No. | CKM00133700906
Model No. | VNX_5400
Software Level | 5.33.184
System Cache (GB) | 32
Fast Cache Enabled | True
Fast Cache (GB) | 275
Total No. Drives | 155
No. SSD Drives | 7
No. HDD Drives | 148
Usable SSD Capacity (TB) | 0.62
Usable HDD Capacity (TB) | 257.0
Subscription % | 93.67%
Subscription Capacity (TB) | 192.96
Used Capacity TB | 187.62
Configured Capacity (TB) | 205.78
LUN Skew - Avg IO | 74.2%
Configuration File Date | 2020-09-14
Performance Start | 2020-09-14 09:54:45
Performance End | 2020-09-21 00:28:25
Performance Interval | 1 mins
Peak IOPS: Date Time | 2020-09-16 01:05:59
Peak IOPS: IOPS | 10294
Peak IOPS: Read % | 81
Peak IOPS: Avg. Read Size (KB) | 24.27
Peak IOPS: Avg. Write Size (KB) | 33.37
Peak IOPS: MB/s | 260.95
Peak IOPS: Latency (ms) | 4.3
95th IOPS: Date Time | 2020-09-16 00:55:12
95th IOPS: IOPS | 5,730
95th IOPS: Read % | 84
95th IOPS: Avg. Read Size (KB) | 23.02
Inventory and Capacity Summary
Workload Summary Peak IOP Measurements
Workload Summary 95th Percentile Measurements
Workload Summary Peak MB/s Measurements
Peak MB/s: Date Time | 2020-09-20 16:09:15
Peak MB/s: IOPS | 5661
Peak MB/s: Read % | 56
Peak MB/s: Avg. Read Size (KB) | 72.39
Peak MB/s: Avg. Write Size (KB) | 89.42
Peak MB/s: MB/s | 441.29
Peak MB/s: Latency (ms) | 14.2
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 3: Summary - MAA-VNX01
Snap View | Yes
Mirror View | Yes
Recover Point | Yes
SAN Copy | Yes
Configuration File Date | 2020-09-14
Performance Start | 2020-09-14 09:55
Performance End | 2020-09-21 00:28
Performance Interval (mins) | 1 mins
FC 4GB | 0
FC 8GB | 4
FC 16GB | 0
1 GigE | 0
10 GigE | 0
iSCSI | 4
File | Yes
Block | Yes
Serial No. | CKM00133700906
Model No. | VNX_5400
Software Level | 5.33.184
System Cache (GB) | 32
No. DAEs | 9
Active Drives | 144
Inactive Drives | 11
Empty Slots | 10
Hardware Overview
Software Features
Input Data
Connectivity
Emulations
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 4: Capacity Summary by Drive Type - MAA-VNX01
Name | Model | Total Raw Capacity (TB) | Usable SSD (TB) | Configured Capacity (TB) | Used (TB) | Utilization (%)
MAA-VNX01 | VNX_5400 | 257.63 | 0.62 | 205.78 | 187.62 | 91
Drive Type | Rotational Speed (K) | Number of Spare Drive | Number of Data Drive | Raw Size (GB) | Number of Drives | Raw Capacity (TB) | Raw Capacity (%)
Empty Slot | Empty | 0 | 0 | 0 | 10 | 0.0 | 0.0
HDD | 7.2 | 3 | 80 | 2,751 | 83 | 222.98 | 86.55
HDD | 10 | 6 | 58 | 536 | 64 | 33.5 | 13.0
HDD | Unknown | 1 | 0 | 536 | 1 | 0.52 | 0.2
SSD | Flash | 1 | 6 | 91 | 7 | 0.62 | 0.24
Copyright © 2020 Dell Inc.
PPTX 2018.08.14
Notes: Utilization (%) is calculated by dividing Used(TB) by Usable (TB). Used/Usable * 100 = Utilization %

## Slide 5: Array Profile Metric - MAA-VNX01
Number of Disks | 155
Usable HDD (TB) | 257
Usable SSD (TB) | 0.62
Raw Capacity (TB) | 257.63
Used Capacity(TB) | 187.62
LUN Skew | 74% of IOPS/26% of LUNS
Front End MB/sec - max | 441
Date Time- Peak | 2020-09-16 01:05:59
IOPS at Peak | 10,294
Read % at Peak | 81.00
Read Size (KB) at Peak | 24.27
Write Size (KB) at Peak | 33.37
MB/sec at Peak | 261
Latency (ms) at Peak | 4.3
Copyright © 2020 Dell Inc.
PPTX 2018.08.14
Notes: SSD is the total RAW physical capacity of the array. LUN is the summation of the total volume size. LUN used is the amount of non-zero data written to the array before compression and deduplication. The rest measures a peak. This slide is designed to show in one slide all of the KPIs for sizing.

## Slide 6: 5 Year Growth Projection - MAA-VNX01
Copyright © 2020 Dell Inc.
At 20% growth, usable capacity will be exceeded in less than 1 year.
PPTX 2018.08.14

## Slide 7: Array Profile Details

## Slide 8: Array Capacity - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 9: Fibre Channel Ports - MAA-VNX01
Name | Speed (Gbit/sec) | Read MB/sec 95th | Write MB/sec 95th
Port 0 [FC; 50:06:01:60:88:60:14:25:50:06:01:60:08:60:14:25 ] | 0 | 0 | 0
Port 0 [FC; 50:06:01:60:88:60:14:25:50:06:01:68:08:60:14:25 ] | 0 | 0 | 0
Port 1 [FC; 50:06:01:60:88:60:14:25:50:06:01:61:08:60:14:25 ] | 0 | 0 | 0
Port 1 [FC; 50:06:01:60:88:60:14:25:50:06:01:69:08:60:14:25 ] | 0 | 0 | 0
Port 2 [FC; 50:06:01:60:88:60:14:25:50:06:01:62:08:60:14:25 ] | 0 | 0 | 0
Port 2 [FC; 50:06:01:60:88:60:14:25:50:06:01:6A:08:60:14:25 ] | 0 | 0 | 0
Port 3 [FC; 50:06:01:60:88:60:14:25:50:06:01:63:08:60:14:25 ] | 0 | 0 | 0
Port 3 [FC; 50:06:01:60:88:60:14:25:50:06:01:6B:08:60:14:25 ] | 0 | 0 | 0
Port 4 [FC; 50:06:01:60:88:60:14:25:50:06:01:64:08:60:14:25 ] | 8 | 31 | 29
Port 4 [FC; 50:06:01:60:88:60:14:25:50:06:01:6C:08:60:14:25 ] | 8 | 44 | 30
Port 5 [FC; 50:06:01:60:88:60:14:25:50:06:01:65:08:60:14:25 ] | 8 | 0 | 1
Port 5 [FC; 50:06:01:60:88:60:14:25:50:06:01:6D:08:60:14:25 ] | 8 | 0 | 0
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 10: Fibre Channel Ports - MAA-VNX01
Name | Speed (Gbit/sec) | Read MB/sec 95th | Write MB/sec 95th
Port 6 [FC; 50:06:01:60:88:60:14:25:50:06:01:66:08:60:14:25 ] | 0 | 0 | 0
Port 6 [FC; 50:06:01:60:88:60:14:25:50:06:01:6E:08:60:14:25 ] | 0 | 0 | 0
Port 7 [FC; 50:06:01:60:88:60:14:25:50:06:01:67:08:60:14:25 ] | 0 | 0 | 0
Port 7 [FC; 50:06:01:60:88:60:14:25:50:06:01:6F:08:60:14:25 ] | 0 | 0 | 0
Port 8 [iSCSI; iqn.1992-04.com.emc:cx.ckm00133700906.a8 ] | 16 | 8 | 4
Port 8 [iSCSI; iqn.1992-04.com.emc:cx.ckm00133700906.b8 ] | 16 | 16 | 9
Port 9 [iSCSI; iqn.1992-04.com.emc:cx.ckm00133700906.a9 ] | 16 | 8 | 4
Port 9 [iSCSI; iqn.1992-04.com.emc:cx.ckm00133700906.b9 ] | 16 | 15 | 9
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 11: Performance Profile - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 12: Front End Ports: Peak Composite
Copyright © 2019 Dell Inc.
Chart: 
26-69% | 30 | 35 | 28
70-89%
90-100%
Chart: 
26-69% | 0 | 28 | 0 | 0 | 0 | 0 | 0 | 26 | 29
70-89% | 0 | 0 | 0 | 0 | 0 | 0
90-100% | 0 | 0 | 0 | 0 | 0 | 0

## Slide 13: Cache Utilization
SP-B
Chart: Cache Flush (MB/s)
Chart: Cache Flush (MB/s)
Copyright © 2019 Dell Inc.
SP-A

## Slide 14: Peak/Average Ports Utilization
Chart: 
| SPA 4 | SPA 5 | SPA 8 | SPA 9
Peak 0-25% | 3 | 9 | 9
Peak 26-69% | 29
Peak 70-89%
Peak 90-100%
Average 0-25% | 1 | 0 | 0 | 0
Average 26-69%
Average 70-89%
Average 90-100%
Baseline | 0 | 0 | 0 | 0
Peak Timestamp
Chart: 
| SPB 4 | SPB 5 | SPB 8 | SPB 9
Peak 0-25% | 0 | 14 | 14
Peak 26-69% | 35
Peak 70-89%
Peak 90-100%
Average 0-25% | 2 | 0 | 1 | 1
Average 26-69%
Average 70-89%
Average 90-100%
Baseline | 0 | 0 | 0 | 0
Peak Timestamp
Copyright © 2019 Dell Inc.
Peak Utilization
Average Utilization
Notes: FE Port Utilization – Avg/Peak

## Slide 15: Storage Processor Utilization
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 16: Front End Latency - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 17: Front End Bandwidth - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 18: Front End IOPS vs Back End IOPS - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 19: Top 3 Clients by IOPS - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 20: Top 3 Clients by IOPS - MAA-VNX01
Client | #LUNs | Used (TB) | Peak IOPS | Response Time (ms) | Front End MB/sec | Read % | Avg IO Size (KB)
Celerra_MAA-CS0-VNX01 | 45 | 24.03 | 7,921 | 7.4 | 29 | 80.96% | 33.61
MAA-ESXi01.l1rtv.l1.nl MAA-ESXi02.l1rtv.l1.nl MAA-ESXi03.l1rtv.l1.nl MAA-ESXi06.l1rtv.l1.nl MAA-ESXi07.l1rtv.l1.nl MAA-ESXi08.l1rtv.l1.nl MAA-ESXi09.l1rtv.l1.nl MAA-ESXi10.l1rtv.l1.nl | 5 | 8.23 | 6,287 | 23.47 | 43 | 54.32% | 42.06
MAA-ESXi04.l1rtv.l1.nl MAA-ESXi05.l1rtv.l1.nl | 3 | 1.26 | 2,432 | 2.95 | 3 | 67.71% | 23.39
PPTX 2018.08.14
Copyright © 2020 Dell Inc.

## Slide 21: IO Size and Read Percent - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 22: IOPS Thresholds - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 23: Back End Activity By Pool - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 24: Back End Activity By Pool - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 25: Back End Activity By Pool - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 26: Total Queue Length - MAA-VNX01
Copyright © 2020 Dell Inc.
PPTX 2018.08.14

## Slide 27: Top Clients and LUNs

## Slide 28: Top 15 LUNs by IOPS - MAA-VNX01
LUN | Front End IOPS - max | Front End MB/sec-max | Avg IO Size (KB) | Latency (ms) - max | Latency (ms) - avg | Read % - avg
LUN-File-NLSAS_16 | 5,848 | 97 | 24.81 | 30.60 | 2.68 | 97.32%
VMware-Productie_0 | 5,607 | 244 | 43.14 | 110.80 | 22.01 | 59.26%
VMware-Productie_1 | 2,852 | 139 | 33.03 | 349.50 | 33.12 | 50.65%
VMware-HorizonView_2 | 2,700 | 165 | 23.39 | 28.10 | 2.94 | 65.13%
VMware-HorizonView_1 | 2,549 | 141 | 21.29 | 31.70 | 2.62 | 64.48%
VMware-Productie_2 | 2,088 | 88 | 20.1 | 133.80 | 18.01 | 48.6%
LUN-File-NLSAS_17 | 1,963 | 78 | 22.2 | 12.50 | 2.65 | 81.76%
VMware-HorizonView_0 | 1,960 | 141 | 29.01 | 28.70 | 2.31 | 72.56%
LUN-File-NLSAS_18 | 1,868 | 79 | 22.61 | 14.50 | 3.14 | 86.01%
LUN-File-NLSAS_20 | 1,782 | 78 | 22.85 | 11.40 | 2.77 | 88.05%
PPTX 2018.08.14
Copyright © 2020 Dell Inc.
Notes: This shows the top 15 LUNS by IOPS

## Slide 29: Top 15 LUNs by IOPS - MAA-VNX01
LUN | Front End IOPS - max | Front End MB/sec-max | Avg IO Size (KB) | Latency (ms) - max | Latency (ms) - avg | Read % - avg
LUN-FIle-NLSAS_19 | 1,736 | 78 | 23.47 | 12.70 | 2.73 | 87.36%
VMware-Productie_3 | 1,590 | 98 | 40.73 | 305.90 | 9.83 | 75.68%
LUN-File-Mixed_5 | 1,284 | 43 | 31.69 | 76.90 | 4.34 | 73.4%
LUN-File-Mixed_3 | 1,249 | 43 | 31.82 | 72.00 | 4.32 | 72.84%
LUN-File-Mixed_2 | 1,246 | 43 | 31.91 | 59.50 | 4.49 | 72.24%
PPTX 2018.08.14
Copyright © 2020 Dell Inc.
Notes: This shows the top 15 LUNS by IOPS

## Slide 30: Top 15 LUNs by MBPS - MAA-VNX01
LUN | Front End IOPS - max | Front End MB/sec-max | Avg IO Size (KB) | Latency (ms) - max | Latency (ms) - avg | Read % - avg
VMware-Productie_0 | 5,607 | 244 | 43.14 | 110.80 | 22.01 | 59.26%
VMware-HorizonView_2 | 2,700 | 165 | 23.39 | 28.10 | 2.94 | 65.13%
VMware-HorizonView_1 | 2,549 | 141 | 21.29 | 31.70 | 2.62 | 64.48%
VMware-HorizonView_0 | 1,960 | 141 | 29.01 | 28.70 | 2.31 | 72.56%
VMware-Productie_1 | 2,852 | 139 | 33.03 | 349.50 | 33.12 | 50.65%
Lun-File-Mixed_17 | 1,203 | 137 | 138.63 | 252.30 | 20.85 | 81.74%
VMware-SQL_0 | 1,033 | 129 | 73.73 | 505.10 | 9.85 | 65.16%
LUN-File-NLSAS_15 | 843 | 120 | 120.91 | 29.00 | 3.31 | 88.49%
VMware-Productie_3 | 1,590 | 98 | 40.73 | 305.90 | 9.83 | 75.68%
LUN-File-NLSAS_16 | 5,848 | 97 | 24.81 | 30.60 | 2.68 | 97.32%
PPTX 2018.08.14
Copyright © 2020 Dell Inc.
Notes: This shows the top 15 LUNS by IOPS

## Slide 31: Top 15 LUNs by MBPS - MAA-VNX01
LUN | Front End IOPS - max | Front End MB/sec-max | Avg IO Size (KB) | Latency (ms) - max | Latency (ms) - avg | Read % - avg
VMware-Productie_2 | 2,088 | 88 | 20.1 | 133.80 | 18.01 | 48.6%
LUN-File-NLSAS_18 | 1,868 | 79 | 22.61 | 14.50 | 3.14 | 86.01%
LUN-FIle-NLSAS_19 | 1,736 | 78 | 23.47 | 12.70 | 2.73 | 87.36%
LUN-File-NLSAS_20 | 1,782 | 78 | 22.85 | 11.40 | 2.77 | 88.05%
LUN-File-NLSAS_17 | 1,963 | 78 | 22.2 | 12.50 | 2.65 | 81.76%
PPTX 2018.08.14
Copyright © 2020 Dell Inc.
Notes: This shows the top 15 LUNS by IOPS