## Slide 1
1080 cm
960 cm
All auto-wet bench systems need to fit in this room, together with other equipment that need to fit in the same room (dark blue and green boxes). The location of the equipment (including the blue and green) is flexible.
Each tile is 60x60 cm

## Slide 2
7800
7200
All auto-wet bench systems need to fit in the blue boxed space. The space to the right is reserved for other equipment that need to fit in the same room. There is some flexibility in optimizing the room layout

## Slide 3: Auto-wet bench configuration options
Option 1:
  5 x (3 etch + 3 rinse + 1 dryer)
    5 process units, each with load tray and dryer, with 1 dedicated unit for processes with metal on wafer
    Most frequently used processes are redundant
Option 2:
  2 x (6 etch + 6 rinse + 1 dryer) + 1 x (3 etch + 3 rinse + 1 dryer)
    3 process units, each with load tray and dryer, with 1 dedicated smaller unit for processes with metal on wafer
    Most frequently used processes are redundant

## Slide 4: Option 1
Buffered HF (BOE) - 7:1 and H3PO4:H2O - 1:9 are used most frequently
Buffered HF (BOE) - 7:1 and Citric Acid:KOH:H2O2 have the longest total process time
QDR = Quick Dump Rinse
System 1 3 etch / 3 rinse | System 2 3 etch / 3 rinse | System 3 3 etch / 3 rinse | System 4 3 etch / 3 rinse | System 5 3 etch / 3 rinse Metal on wafer
Buffered HF (BOE) - 7:1 | H3PO4:H2O - 1:9 | Citric Acid:KOH:H2O2 | Buffered HF (BOE) - 7:1 | HF 1%
QDR | QDR | QDR | QDR | QDR
HF 1% | HCl:H3PO4 - 1:10 | H2SO4:H2O2:H2O - 1:1:10 | H3PO4:H2O - 1:9 | H2O:H3PO4:HCl - 9:1:1
QDR | QDR | QDR | QDR | QDR
H2SO4 | HCl:H3PO4 - 1:4 | H3PO4:H2O2:H2O - 1:8:60 | H2SO4:H2O2:H2O - 1:1:100 | Iron(III) chloride 27,5% (FeCl3:H2O)
QDR | QDR | QDR | QDR | QDR
Dryer | Dryer | Dryer | Dryer | Dryer

## Slide 5: Option 2
System 1 6 etch / 6 rinse | System 2 6 etch / 6 rinse | System 3 3 etch / 3 rinse Metal on wafer
Buffered HF (BOE) - 7:1 | HCl:H3PO4 - 1:4 | HF 1%
QDR | QDR | QDR
H3PO4:H2O - 1:9 | HCl:H3PO4 - 1:10 | H2O:H3PO4:HCl - 9:1:1
QDR | QDR | QDR
H2SO4 | H3PO4:H2O - 1:9 | Iron(III) chloride 27,5% (FeCl3:H2O)
QDR | QDR | QDR
Citric Acid:KOH:H2O2 | H2SO4:H2O2:H2O - 1:1:100 | Dryer
QDR | QDR | 
H2SO4:H2O2:H2O - 1:1:10 | Buffered HF (BOE) - 7:1 | 
QDR | QDR | 
H3PO4:H2O2:H2O - 1:8:60 | HF 1% | 
QDR | QDR | 
Dryer | Dryer |